## Slide 1
SMART GARBAGE
OVERFLOW DETECTION SYSTEM
Using IoT (WiFi) — NodeMCU ESP8266 & Ultrasonic Sensor
Kevin Jason D | Krishnaraja D | Kathirvel K | Hemanth E | Madhesh G
Tagore Engineering College · Anna University · May 2026
B.E. Computer Science and Engineering
IoT · WiFi · Ultrasonic Sensing · Smart City · Waste Management

## Slide 2
ABSTRACT
🌆 Waste management is a critical challenge in modern urban cities with rapidly growing solid waste volumes.
🔌 Our IoT-based system uses an HC-SR04 ultrasonic sensor + NodeMCU ESP8266 to monitor garbage fill levels in real-time.
📶 When the bin is full, the system activates LED & buzzer alerts and sends WiFi notifications to a mobile app.
✅ Results: ±1% measurement accuracy, ~110ms alert response, 7-day battery life, WiFi range up to 100 meters.
💡 Total cost: under ₹600 (US$7-8) — making mass deployment viable for smart city waste management programs.
Keywords: Smart garbage system · IoT · Ultrasonic sensor · NodeMCU ESP8266 · WiFi · Waste management · Smart city

## Slide 3
PROBLEM STATEMENT & OBJECTIVES
PROBLEMS WITH TRADITIONAL SYSTEMS
✗ Fixed schedules → overflow when bins fill faster
✗ No real-time visibility into actual fill levels
✗ Fuel wastage from inefficient collection routes
✗ Health hazards: pests, disease vectors from overflow
✗ No data for decision-making or route optimization
OUR OBJECTIVES
✓ Low-cost IoT system for real-time garbage monitoring
✓ HC-SR04 ultrasonic sensor for accurate level detection
✓ NodeMCU ESP8266 as central processor with built-in WiFi
✓ LED + buzzer alerts when bins reach capacity
✓ Wireless cloud/mobile app status transmission
✓ Prove feasibility for smart city implementation

## Slide 4
PROPOSED SYSTEM ARCHITECTURE
SENSING LAYER
• HC-SR04 Ultrasonic Sensor
• Measures distance to garbage
• 40kHz pulses, ±2cm accuracy
▶
PROCESSING LAYER
• NodeMCU ESP8266
• Calculates fill percentage
• Threshold comparison logic
▶
ALERT LAYER
• LED Indicator (visual)
• Buzzer (audio alert)
• Activated at thresholds
▶
NETWORK LAYER
• WiFi (802.11 b/g/n)
• HTTP / MQTT protocol
• Up to 100m range
▶
APPLICATION LAYER
• Cloud platform / ThingSpeak
• Mobile app notifications
• Real-time dashboard
SYSTEM OVERVIEW
The ultrasonic sensor measures the gap between sensor (bin top) and garbage surface. NodeMCU processes data every 2 seconds.
FULL_THRESHOLD = 10cm → rapid blink + continuous buzz + WiFi alert | WARN_THRESHOLD = 18cm → slow blink + pulsed buzz | Normal ≥ 18cm → no alert

## Slide 5
COMPONENT DESCRIPTION
NodeMCU ESP8266
▸ 32-bit Tensilica CPU @ 80/160MHz
▸ 160KB RAM, 4MB Flash
▸ 802.11 b/g/n WiFi built-in
▸ 11 GPIO pins, 1 ADC
▸ 80–160mA active, 0.015mA sleep
HC-SR04 Ultrasonic Sensor
▸ Operating frequency: 40kHz
▸ Range: 2–400cm, ±2cm accuracy
▸ Resolution: 0.3cm
▸ 5V DC, 15mA current draw
▸ Cone angle: 15°
LED + Buzzer
▸ LED: 2.0–2.2V forward, 20mA
▸ 100,000+ hour LED lifespan
▸ Buzzer: 5V, 2–2.5kHz, 85dB
▸ Visual + audio dual alert
▸ Series resistor protection
Power Supply
▸ 5V USB for stationary use
▸ 9V battery + LM7805 regulator
▸ 2–3 day runtime (WiFi on)
▸ 7–10 day runtime (WiFi off)
▸ Brownout protection at 4.5V
All components are commercially available, low-cost, and well-documented for Arduino/NodeMCU development.

## Slide 6
WORKING PRINCIPLE & CIRCUIT
SENSOR OPERATION
1. 10µs trigger pulse sent to TRIG pin
2. Sensor emits 40kHz ultrasonic pulse
3. Sound reflects off garbage → returns to receiver
Distance (cm) = (echo_duration × 0.034) / 2
CIRCUIT CONNECTIONS
⮕ HC-SR04 TRIG → NodeMCU D6 (GPIO12)
⮕ HC-SR04 ECHO → NodeMCU D7 (GPIO13)
⮕ HC-SR04 VCC/GND → NodeMCU 5V/GND
⮕ LED Anode → NodeMCU D1 (GPIO5) via 220Ω
⮕ Buzzer (+) → NodeMCU D2 (GPIO4)
ALERT THRESHOLDS
Distance
Status
LED
Buzzer
> 18 cm
Normal
Off
Off
10–18 cm
Warning
2 blinks/5s
Pulsed
< 10 cm
FULL
5 rapid blinks
Continuous
JSON PAYLOAD SENT VIA WiFi
{ "bin_id": "BIN_001",
"status": "warning",
"fill_pct": 65,
"distance_cm": 12.5,
"timestamp": "2026-05-02T10:30:45Z" }

## Slide 7
RESULTS & DISCUSSION
Sensor Accuracy Test
Actual (cm)
Reading (cm)
Error (cm)
Error %
10
10.1
+0.1
1.0%
20
19.9
−0.1
0.5%
30
30.2
+0.2
0.67%
50
49.8
−0.2
0.4%
80
80.5
+0.5
0.63%
Response Time
Sensor reading → LED/Buzzer alert: ~110ms
All state transitions tested and confirmed.
Power Consumption
Chart: 
| WiFi TX | Sensor Read | LED/Buzzer | Idle/Sleep
Avg mA | 8 | 2 | 1.5 | 12.3
Total Average: 23.8mA → Battery Life: ~84 hours (3.5 days) with WiFi on, 7–10 days with WiFi off (2000mAh battery)
WiFi range: 100m LOS / 50m through walls · Works 5–50°C · Up to 95% RH humidity

## Slide 8
COST ANALYSIS & COMPARISON
Bill of Materials
Component
Cost (₹)
NodeMCU ESP8266
₹250
Ultrasonic Sensor (HC-SR04)
₹80
LED
₹10
Buzzer
₹30
Breadboard
₹60
Jumper Wires (×10)
₹50
Dustbin Model
₹100
TOTAL
₹600
Chart: 
| NodeMCU | HC-SR04 | Dustbin | Breadboard | Jumper Wires | Buzzer | LED
Cost | 250 | 80 | 100 | 60 | 50 | 30 | 10
Comparison with Alternatives
Feature
This Project
Commercial IoT Bin
Traditional
Cost/Unit
₹600 (~$7)
₹5,000–15,000
₹300 (bin only)
Monitoring
Real-time
Real-time
Manual
Installation
15 minutes
30–60 min
N/A
ROI Period
6–12 months
18–24 months
—

## Slide 9
CONCLUSION & FUTURE WORK
KEY CONCLUSIONS
✓ HC-SR04 achieves ±1% measurement accuracy across 10–80cm range — ideal for bin monitoring
✓ NodeMCU ESP8266 is cost-effective and capable for low-power IoT applications
✓ ~110ms response time from threshold breach to full alert activation
✓ Battery-powered 2–3 days (WiFi on) / 7–10 days (WiFi off) — sufficient for urban deployment
✓ Total cost under ₹600 proves economic viability for smart city mass-deployment
FUTURE ENHANCEMENTS
☁️ Cloud Dashboard
Real-time web-based monitoring for all bins citywide
☀️ Solar Power
2–5W panel + charging for perpetual off-grid operation
📡 LoRaWAN
Long-range connectivity for entire city-district coverage
🤖 Machine Learning
Predict fill times and optimize collection routes with AI
Smart Garbage Overflow Detection System · Tagore Engineering College · Anna University · May 2026